Serial Control Message

# Serial Control Message Communication
Serial Control Message (‘SCM’ further in this document) Communication is initiated from PC (Python script or Linux GUI App) to deliver controlling commands to a FLX device (primarily Handle Controller) via serial port (USB) for development purposes and test automation.
## Serialized SCM Format
### Table 1. Serialized Wire Message Format
Field and Size in bytes			Comments	References (source code)
Message Prefix		3	Common start transmission indicator, reserved: ‘B’,’g’,’n’	flxbot-firmware/flx/include/flx/communications/serial/ros_wire_message.hpp
Message type		1	Message type for serial control communication reserved value 10 (decimal) equal to “String” in FLX message types
crc8		1	Standard CRC8 algorithm calculated for the first 4 bytes
serialized payload	command type	1	Reserved value 42 (decimal) for further extensions	flxbot-firmware/flx/include/flx/communications/serial/serial_command_type.hpp
	command id	1	Reserved command ID as defined by Table 2.
	command payload size	1	[0..8] value indicating following command payload
	command payload	-	Variable command dependent serialized payload up to 8 bytes inclusive
crc16		2	Standard CRC16 algorithm calculated for the whole serialized payload

## Commands Format and payload
### Table 2. Serial Command Format and payload
Command name	Command ID	Payload
Joystick button click (single)	‘K’	none
LEFT (Joystick single move)	‘L’	none
RIGHT (Joystick single move)	‘R’	none
UP (Joystick single move)	‘U’	none
DOWN (Joystick single move)	‘D’	none
Rear button click (single)	‘r’	none
Joystick BendRotateVelocityTarget	‘B’	8 bytes as defined in Table 5.
Joystick PanTiltVelocityTarget	‘P’	8 bytes as defined in Table 5.

## Joystick direction & velocity
### Velocity values

struct VelocityTarget {
    float velocity; // range [-5.0..5.0]
    float acceleration; // range [-5.0..5.0]
    float max_velocity; // range [-5.0..5.0]
    float max_acceleration; // range [-5.0..5.0]
};

### Serialized binary payload for velocity
Due to limited range of the values of type float, the value can be compressed into the single byte, as listed in the Table below.
### Table 3. Serialized Wire velocity
Field	bytes	Serialization
Joystick move payload {
velocity	1	Each byte is serialized MSBF as follows: / structure serialized_float { / uint8_t reserved : 1; // reserved / uint8_t sign : 1; // if 1 then negative / uint8_t integer : 3; // range [0..7] / uint8_t fraction : 3; // range [0..7] / };
acceleration	1
max_velocity	1
max_acceleration	1
}; // 4 bytes total

### Table 4. Serialized Wire Message for Joystick Move commands
Field		Size (bytes)	Value
start_transmission		3	0x42 0x67 0x6E # 'Bgn'
message_type		1	0x0A # '\n' type 10 (decimal) ’String’
crc8		1	0x71 # 'q' CRC8
payload	command_type	1	0x2A # '42' command type
	command_id	1	0xXX # ‘B’ or ‘P’ command for joystick
	Bend	4	[XX XX XX XX] # example: 0x05, 0x45, 0x28, 0x4a,
	Rotate	4	[XX XX XX XX] # example: 0x05, 0x45, 0x28, 0x4a,
crc16		2	Standard CRC16 algorithm calculated for 8 bytes of payload

## SCM script format
All script commands are case-sensitive text in json format shown below. The following Table represents textual values and options.
### Table 5. Command script formats (json)
Command	In script	Comments
Joystick button click	OK	{ / "_comment": "This is example of Joystick Button click", / "command": "OK", / "expected": "Bend & Rotate", / "timeout": "2" / }, / optional field “expected” define expected navigation position report from the device for synchronization. If omitted then no feedback is expected. / Optional timeout defines waiting time after command submission to receive feedback from the device; if omitted default value “1” second is used
joystick Left	Left
Joystick Right	Right
Joystick Up	UP
Joystick Down	Down
Rear button click	Rear
Joystick move	Bend	Joystick Bend & Rotate Velocity Target
	Pan	Joystick Pan & Tilt Velocity Target

### Script file example
{
    "_comment": "This is example of Joystick Button press",
    "command": "OK",
    "expected": "Bend & Rotate",
    "timeout": "2"
},
{
    "_comment": "This is example of Rear Button press",
    "command": "Rear",
    "expected": "Bend & Rotate Segment",
    "timeout": "3"
},
{
    "_comment": "This is example of Joystick Right move",
    "command": "Right",
    "expected": "LED Lights",
    "timeout": "2"
},
{
    "_comment": "This is example of Joystick Left move",
    "command": "Left",
    "expected": "Bend & Rotate",
    "timeout": "1"
},
{
    "_comment": "This is example of Joystick Bend & Rotate command",
    "command": "Bend",
    "timeout": "1",
    "payload": {
        "bend": {
        "velocity": "1.0",
        "acceleration": "0.0",
        "max_velocity": "1.0",
        "max_acceleration": "1.0"
        },
        "rotate": {
        "velocity": "0.5",
        "acceleration": "0.0",
        "max_velocity": "1.0",
        "max_acceleration": "1.0"
        }
    }
},
{
    "_comment": "This is example of missing parameter: no feedback expected",
    "command": "Up",
    "timeout": "2"
},
{
    "_comment": "This is example of missing parameter: deault timeout 1",
    "command": "Down",
    "expected": "LED Lights",
}